## Slide 1
Optical Fibers
Piotr Turowicz
Poznan Supercomputing and Networking Center
piotrek@man.poznan.pl
.
http://www.porta-optica.org

## Slide 2: Content
Basics of optical fiber transmission
FO connetcors
Fiber Types, Fiber standards
Optical Power, Optical budget
WDM technology
PIONIER and POZMAN Optical Network
FO testing

## Slide 3: Introduction
Optical communication is as old as humanity itself, since from time immemorial optical messages have been exchanged, e.g. in the form of:
    hand signals
    smoke signals
    by optical telegraph
To the optical information technology as we know it today - two developments were crucial:
    The transmission of light over an optically transparent matter (1870 first attempts by Mister Tyndall, 1970 first FO by Fa. Corning)
    Availability of the LASER, in 1960

## Slide 4: The principle
The principle of an optical communication system
Transmission
channel
Tx
E
O
Rx
O
E
Receiver
Converter
Transmitter
Converter
Optical transmission length is restricted by the attenuation or dispersion.

## Slide 5: The electromagnetic wave
Electric wave
Magnetic wave
Propagation
direction [meters]
Wavelength 
Time scale
[seconds]
Period 
Frequency = 1 / 
Light is an electromagnetic wave and can be described with Maxwell’s equations.

## Slide 6
Wavelength range of electromagnetic transmission
Wavelength
Frequency [Hz]
102 103 104 105 106 107 108 109 1010 1011 1012 1013 1014 1015 1016 1017 1018
3000km 30km 300m 3m 3cm 0.3mm 3m 30nm 0.3nm
NF
range
HF
range
Microwave
range
Optical
range
X-Ray
range
Analog
telephony
AM
radio
TV &
FM
radio
Mobile
phone
MW
stove
X-Ray
pictures

## Slide 7: Wavelength range of optical transmission
3. optical window
Infrared
range
Visible
range
Singlemode (1310 – 1650nm)
GOF Multimode (850 – 1300nm)
POF (520 – 650nm)
PCF (650 – 850nm)
1. optical window
1800 1600 1400 1200 1000 800 600 400
Wavelength [nm]
2. optical window

## Slide 8: Multi-Mode vs Single-Mode
 | Multi-Mode | Single-Mode
Modes of light | Many | One
Distance | Short | Long
Bandwidth | Low | High
Typical Application | Access | Metro, Core
Notes: MM fibers are typically used for small distances (a few kms) whereas SM fibers for long distance.
SM fibers can carry a few Tbps by deploying DWDM technology in comparison to MM fibers that are typically used for providing access to clients (order of Gbps)

## Slide 9
Velocity of electromagnetic wave
Speed of light (electromagnetic radiation) is:
C0 = Wavelength x frequency
C0 = 299793 km / s
Remarks: An x-ray-beam ( = 0.3 nm), a radar-beam ( = 10 cm ~ 3 GHz) or
an infrared-beam ( = 840 nm) have the same velocity in vacuum
(Speed of light in vacuum)

## Slide 10: Refractive index
(Change of velocity of light in matter)
Velocity of light (electromagnetic radiation) is:
always smaller than in vacuum, it is
Cn (Velocity of Light in Matter)
n = C0 / Cn
n is defined as refractive index (n = 1 in Vacuum)
n is dependent on density of matter and wavelength
Remarks: nAir= 1.0003; ncore= 1.5000 or nssugar Water= 1.8300

## Slide 11: Refraction
light beam
1
2
Glass material
with slightly
higher density
Glass material
with slightly
lower density
n2
n1
Remarks: n1 < n2 and 1 > 2
sin 2 / sin 1 = n1 / n2
Plane of interface

## Slide 12: Total refraction
light beam
1 = 90°
L
Glass material
with slightly
higher density
Glass material
with slightly
lower density
n2
n1
Remarks: n1 < n2 and 2 = L
Critical angle
sin 1 = 1
sin L = n1 / n2
Plane of interface
Incident light has angle = critical

## Slide 13: Transmission Bands
Optical transmission is conducted in wavelength regions, called “bands”.
Commercial DWDM systems typically transmit at the C-band
  Mainly because of the Erbium-Doped Fiber Amplifiers (EDFA).
Commercial CWDM systems typically transmit at the S, C and L bands.
ITU-T has defined the wavelength grid for xWDM transmission
  G.694.1 recommendation for DWDM transmission, covering S, C and L bands.
  G.694.2 recommendation for CWDM transmission, covering O, E, S, C and L bands.
Band | Wavelength (nm)
O | 1260 – 1360
E | 1360 – 1460
S | 1460 – 1530
C | 1530 – 1565
L | 1565 – 1625
U | 1625 – 1675

## Slide 14: Reflection
light beam
in
Glass material
with slightly
lower density
n2
n1
Remarks: n1 < n2 and in = out
out
Glass material
with slightly
higher density
Plane of interface
Incident light has angle > critical

## Slide 15
Summary
n2
out
Glass material
with slightly
lower density
in
Glass material
with slightly
higher density
n1
2
2
1

refraction
Total
refraction
reflection
Plane of Interface

## Slide 16: Numerical Aperture (NA)
Light rays outside acceptance angle leak out of core
Light rays in this angle are guided in core
NA = (n22 – n21) = sin 
Standard SI-POF = NA 0.5 → 30°
Low NA SI-POF = NA 0.3 → 17.5°

## Slide 17: Fiber structure
Primary Coating (protection)
Cladding
Core (denser material, higher N/A)
Light entrance
cone N.A.
(Numerical Aperture)
Lost light
Lost light
n1
n1
n2
Refractive index
profile
n1
n2

## Slide 18: Cutoff wavelength
It’s the minimum wavelength above which the SM fiber propagates only one mode. Cutoff wavelength depends on:
Length
Bending radius
Cable manufacturing process

## Slide 19: Fiber and cladding material
 | Glass Optical Fiber (GOF) | Polymer Clad Fiber (PCF) | Polymer Optical Fiber (POF)
Core | Silica | Silica | Polymer
Cladding | Silica | Polymer | Polymer
Where the same material (silica, polymer) is used for core and cladding one of it must be doped during production process to change its refractive index.

## Slide 20: Single Mode Fiber Standards
ITU-T Standard | Name | Typical Attenuation value (C-band) | Typical CD value (C-band) | Applicability
G.652 | standard Single Mode Fiber | 0.25dB/km | 17 ps/nm-km | OK for xWDM
G.652c | Low Water Peak SMF | 0.25dB/km | 17 ps/nm-km | Good for CWDM
G.653 | Dispersion-Shifted Fiber (DSF) | 0.25dB/km | 0 ps/nm-km | Bad for xWDM
G.655 | Non-Zero Dispersion-Shifted Fiber (NZDSF) | 0.25dB/km | 4.5 ps/nm-km | Good for DWDM

## Slide 21: Refractive index profiles
Step Index (SI)
core = Constant refractive index
Multistep Index (MSI)
Core = several layer of material with different refractive indexes
Graded index (GI)
Core = parabolic index
GOF & POF
GOF & POF
POF

## Slide 22: Type of fibers
Optical fiber
Step Index (SI)
Graded Index (GI)
Single mode (SM)
Multi mode (MM)
Multi mode (MM)
9/125µm (GOF) Low water peak Dispersion shifted Non Zero Dispersion Shifted
980/1000 µm (POF) - 500/750 µm (POF) - 200/230 µm (PCF)
50/125 µm (GOF) - 62.5/125 µm (GOF) - 120/490 µm (POF)

## Slide 23: Light in fiber optics propagates on discrete ways
These discrete ways are called modes (in mathematical terms they are the solutions to the Maxwell equations).
Linear
Sinusoidal
Helical

## Slide 24: Multimode fibers (Step index profile)
Refractive index
profile
(Step index)
Remarks: ~ 680 Modes at NA = 0.2, d = 50 m &  = 850 nm
~ 292 Modes at NA = 0.2, d = 50 m & = 1300 nm
Number of modes M = 0.5x(xdxNA/)2
n1
n2
n1
n2
n1
Same core density makes modes’ speed different
(every mode travels for a different length)
Input
Output

## Slide 25: Multimode fibers (Graded index profile)
n1
n1
Refractive index
profile
(Graded Index)
Remarks: ~150 Modes at NA = 0.2, d = 50 m &  = 1300 nm
Number of modes M = 0.25x(xdxNA/)2
Different core density makes modes’ speed same
(every mode travels for about same length)
Input
Output
n1
n2
n2

## Slide 26: Single-mode fiber
Refractive index
profile
(Step Index)
Example: n1 = 1.4570
n2 = 1.4625
Remarks: One mode (2 polarizations)
n1
n2
n1
n1
n2
Input
Output

## Slide 27: Step index and depressed step index
n1
n2
n1
n2
Cladding with
homogeneous
refractive index
OVD process
Cladding with two
refractive indexes
MCVD process dependent
Less macrobending
Wide low attenuation spectrum
Two zero dispersion points

## Slide 28: Types of refractive index profile
Step index
Step index
Graded index
singlemode
transmission
multimode
transmission
multimode
transmission
Output signal
Input signal
n1
n2
r
n1
n2
r
n1
n2
r

## Slide 29: Optical characteristics
1
2
3
Attenuation [dB]
Dispersion
Numerical Aperture (NA) [-]
Power loss along
the optical link
Pulse broadening and signal weakening
Coupling loss LED/Laser  fiber fiber  fiber fiber  e.g. APD*
Transmission
distance
Signal bandwidth & transmission distance
Coupling
capacitance
Term
Effect
Limitation

## Slide 30: NA and transmission performance
Large value of NA mean large value of acceptance angle (
Large value of NA means more light power/modes in the fiber
More modes mean higher mode dispersion (lower bandwidth)
Large values of NA mean lower bending induced attenuation of the fiber
Remarks: Two Fibers with NA = 0.2 & 0.4 Fiber with NA = 0.2 has 8-times more
bending induced attenuation than NA = 0.4 Fiber

## Slide 31: Dispersion (time)
Dispersion are all effects that considerably influence pulse „widening“ and pulse „flattening“.
Input pulse
L1
L2 + L2
L1 + L2 + L3
Output pulse after Lx
The dispersion increases with longer fiber length and/or higher bit rate.

## Slide 32: Dispersion
Modal dispersion Profile dispersion
Chromatic dispersion [ps/km * nm]
Polarisation Modal dispersion PMD [ps/(km)]
Multimode fiber
Single-mode fiber
Dispersion is the widening and overlapping of the light pulses in a optical fiber due to time delay differences.

## Slide 33: Modal dispersion
Step index profile
Delay of modes in the fiber
Lowest-order mode propagates along the optical axis.
Highest-order mode extended length lowest speed
MM Fiber with step index (SI) profile
V = constant refractive index
Large propagation delay → low bandwidth
e.g. PMMA SI-POF, DS-POF

## Slide 34: Profile dispersion
Parabolic index profile
Increase speed of rays near margin
Time differences between low and high order modes is minimizes
MM Fiber with graded index (GI) profile
V2>V1 parabolic index
“no” propagation delay → high bandwidth
e.g. GI-GOF, GI-POF

## Slide 35: Non linear characteristics
SPM - self phase modulation
predominant in SM and power dependent
XFM - cross phase modulation
similar to NEXT but occurring in WDM with adjacent channels
FWM - Four-Wave Mixing
intermodulation between three wavelength creating a fourth one (WDM)
SRS - stimulated Raman scattering
SRB - stimulated Brillouin scattering

## Slide 36: Waveguide dispersion
2w0 Beam waste
Acceptance angle
Numerical Aperture:
NA = sin = (n22 - n12)0.5 =  w0
Example: NA = 0.17 and = 9.8°
Waveguide dispersion occurs when the mode filed is entering into the cladding.
It is wavelength and fiber size dependent.
80% of light in the core
20% of the light in the cladding

Mode field diameter
2w0

## Slide 37: Material dispersion
Since light source has a spectral width (different wavelength).
Since each wavelength has a different speed within an homogeneous material optical pulses result widened because of time dispersion
Density
60-100nm
λ

## Slide 38: Chromatic dispersion
Singlemode chromatic dispersion
Dominant type of dispersion in SM fibers and is caused by wavelength dependent effects.
Chromatic dispersion is the cumulative effect of material and waveguide dispersion
Multimode chromatic dispersion
As waveguide dispersion is very low compared to material dispersion it can be disregarded.

## Slide 39: Polarization mode dispersion (PMD)
"slow axis" ny
"fast axis"nx< n y
y
x
Delay (PMD)
PMD occurs in SM fibers
high bit rate systems
systems with a very small chromatic dispersion
A mode in SM fiber has two orthogonal polarizations

## Slide 40: Bandwidth length product
Bandwidth describes the usable frequency range within a channel
Bandwidth is length dependent because of signal widening (dispersion)
  Pulse widening limits bandwidth B
and the maximum transmission rate Mbps
  Pulse widening is approx. proportional to the fiber length L

## Slide 41: Attenuation
Attenuation is the reduction of the optical power due to
Fiber
Bending
Connection
Attenuation is measured in decibel (dB) and is cumulative
Pin
Pout

## Slide 42: Decibel
In fiber optics signal losses occur as function of fiber length and wave length.
They are called attenuation.
The attenuation is length dependent:
A = 10 x log (Pin / Pout)
Fiber length [km]
Attenuation [dB]
1/2
1/2
3 dB
6 dB
0 dB
100%
50%
25%
Pin
Pout

## Slide 43: Attenuation
Fiber (material)
Absorption Scattering
Connection (fiber end to fiber end)
intristic extrinsic
Bending (fiber and cable)
Microbending Macrobending

## Slide 44: Fiber attenuation
Material absorption 3 to 5% of Attenuation
(can not be influenced by installer)
due to chemical doping process impurity
Residual OH (water peak)
absorb energy and transform it in heat/vibration
greater at shorter wavelength
Rayleigh scattering 96% of Attenuation
(can not be influenced by installer)
due to glass impurity
reflects light in other direction
depending on size of particles
depends on wavelength (>800nm)
Particles
Light waves
Light scattering

## Slide 45: Attenuation spectrum GOF
800 1000 1200 1400 1600
wavelength [nm]
3.5
2.5
1.5
Attenuation [dB/km]
3. Window
1550 nm
SiOH-absorptions
Rayleigh-scattering (~ 1/
950
1240
1440
5.
Window
4. Window
1625 nm
1.
window
850 nm
2.
window
1310 nm

## Slide 46: Connection attenuation
Connection attenuation is the loss of a mechanical coupling of two fibers
caused due to
different fiber parameter → INTRINSIC
connections technique → EXTRINSIC

## Slide 47: Insertion loss - intrinsic
Differences in
Core diameter
Numerical aperture
Refractive index profile

## Slide 48: Insertion loss - extrinsic
Due to
Lateral offset
Axial separation
Axial tilt

## Slide 49: Insertion loss - extrinsic
Due to:
Fresnel reflection
Surface roughness

## Slide 50: Bending attenuation
Micro-bending (can not be influenced by installer)
Cable production process caused by
imperfections in the core/cladding interface
Macro-bending (can be influenced by installer)
Bending diameter < 15x cable dia
Macro-bending is not only increasing the attenuation it also shortens lifetime of a fiber (micro cracks)

## Slide 51: Summary
Light propagation (transmission) into the fiber is affected mostly by:
  attenuation fiber physical characteristic dependent
fiber installation/termination
  dispersion fiber physical characteristic dependent
  non linear effects transmission technology dependent
Transmission optimization process is based on minimizing these parameters by selecting the right media and considering also the related phenomenon:
  light generation
  light injection
  light detection

## Slide 52: From light to bits transmission
Speed is the keyword
Transmission speed is not bits velocity but bits quantity
Quantity in a limited capacity media requires optimization of the media itself
Being media capacity fixed, time is the only variable to play with
For transmission purposes time has two aspects
Slot (on the Media) allocated for each transmitter
Frequency of the transmitter (carrier signal)

## Slide 53: MULTIPLEXING SIGNALS
Optimization of Media is realized by Multiplexing (MUX) and Demultiplexing (DE-MUX)
Over a single media
To get again the same multiple signals
MUX
DE-MUX

## Slide 54: Multiplexing
Electrical signals can be multiplexed using their physical characteristics:
TIME Division Multiplexing
FREQUENCY Division Multiplexing
FDM in F.O. is called Wave Division Multiplexing
Coarse Wave Division Multiplexing
Dense Wave Division Multiplexing
< 8 λ =
> 8 λ =

## Slide 55: TDM concept
Originally designed for voice
Used to transmit OC 48 (2.5Gbps)
Expandable in theory to OC 192 (10Gbps) and OC 768 (40Gbps)
Chromatic dispersion, PMD, non linear effects do not allow economic expansion

## Slide 56: WDM concept and DWDM
Capacity increases by changing wavelengths or assigning a certain frequency to each channel or assigning a color to the light.
DWDM spaces wavelength more densely increasing the number of channels.
The maximum number of wavelengths that can enter a SM fiber is not known yet

## Slide 57: Data transmission with WDM
Fields of Application:
WDMs ( Wavelength Division Multiplex) are used in fiber optics networks for communications and data transmission (cable TV, telephony etc.) to multiply transmitting capacity per optical fiber and lead to cost reduction.
With classical WDM systems a few wavelengths are transmitted via a singlemode fiber.

## Slide 58: Data transmission with WDM
In unidirectional systems the signals from two transmitters with different wavelengths are combined by means of a WDM at the beginning of a transmission path (multiplexing).
1. Unidirectional Transmission (fig. 1):
Bidirectional transmission systems allow single-fiber transmissions at different wavelengths that are independent of each other. The high isolation level of the WDMs provides protection of the laser diodes from the light of the laser operating in the opposite direction.
2. Bidirectional Transmission (fig. 2):

## Slide 59: Data transmission with WDM
The Isolation of WDM are available in different sizes. At this point the isolation of the two wavelengths from
each other must be very high in order to avoid crosstalk.
(This information has to be gathered from the data sheets of the manufacturer )

## Slide 60: Example of WDM Module Datasheet
(normaly the Modules have the better isolation)

## Slide 61: Example of WDM Datasheet

## Slide 62: References
Reichle & De-Massari