## Slide 1
Polarisation Mode Dispersion
Measurement
Piotr Turowicz
Poznan Supercomputing and Networking Center
piotrek@man.poznan.pl
Kiev
9-10 October 2006

## Slide 2
Equipment requirements.
FTB-400 mainframe equipped with GP-407.
FTB-5500B PMD analyzer
FLS-5800-xx series CD/PMD source
Toolbox office software 6.21 or higher installed on FTB-400

## Slide 3
Step 1.
The FLS-5800 series source should be powered-up and allowed to complete its self test routine (less than 30 seconds). The user then has to select wavelength range and then activate the source.
C band (nominally 1510 to 1560nm) and C+L band (nominally 1510 to 1610nm).
Step 2.
Inspect and clean the connectors on the appropriate patch-cord and
connect to the source.
Step 3.
Power-on the FTB-400 and activate the FTB-5800
Step 4.
Connect the patch-cord to the input on the FTB-5800 analyser module.

## Slide 4: Connecting and taking a measurement
Step 1.
The FLS-5800 series source should be powered-up and allowed to complete its self test routine.
The user then has to select wavelength range and then activate the source. There are two options:
C band (nominally 1510 to 1560nm) and
C+L band (nominally 1510 to 1610nm).
Step 2.
Power-on the FTB-400 and activate the FTB-5500B PMD analyser software.
Step 3.
Inspect and clean the connectors on the appropriate patch-cord and connect to the source.

## Slide 5: Connecting and taking a measurement
Step 5.
Check the input power level on the analyzer software. This is a basic Go/No Go indication to indicate if useable power is present before starting. This will save you time in your testing as it will indicate whether:
your source is truly activated,
if you are connected to the correct fibre
(a common problem!)
and can potentially tell you to use longer averaging times
(if the source signal is low)

## Slide 6: Connecting and taking a measurement
Step 8
In Fiber Parameters enter the length of the link in km, select fibre type and select the wavelength range to match your FLS-5800 source settings:
The usual settings are either C+L band or O, C & L. Check the display of the FLS-5800 series source to verify.

## Slide 7: Connecting and taking a measurement
Step 10
To begin a measurement, press the GREEN start button. The software automatically switches to the Results Graph screen. Note - This screen shot shows the typical data AFTER acquisition has finished and the data analysed.

## Slide 8: Connecting and taking a measurement
Step 11
The output of the measurement gives the resultant interferogram, the PMD Delay in [ps] and the PMD Coefficient in [ps/Sqrt_km].
Additional information included in the output includes 2nd Order PMD, Length of sample and Wavelength range over which measurement has been performed.

## Slide 9: References