## Slide 1
Fiber Optic Connections
http://www.porta-optica.org
Piotr Turowicz
piotrek@man.poznan.pl
Poznan Supercomputing and Networking Center
9-10 October 2006

## Slide 2: Fiber optic theory/ connection technique
Three possible options to join fiber, depending on application:
  Detachable connection (patch panel, terminal outlet)
  Quasi-detachable connection (connecting trunks)
  Non-detachable connection (under the sea/ underground)
Connection choice is also dependent on:
  Optical limits imposed but the application/available power budget
  Reliability
  Flexibility
  Costs
  Cable type to be connected

## Slide 3: Overview
Dependent on the Connector Type and polishing (PC, SPC, UPC, APV = HRL)
PC
Physical Contact, Return loss of approximately 30 dB, can be reached by manual polishing
SPC
Super Physical Contact, Return loss of approximately 40dB, can be reached by machine polishing
UPC
Ultra Physical Contact, Return loss of approximately 50 dB, can be reached by machine polishing
and optical testing of the fiber positioning
APC (HRL)
Angle Physical Contact (High Return Loss), Return loss of approximately 60dB
can be reached by machine polishing (usually R. 8° Angle Polished)

## Slide 4: Process challenges: Insertion loss
4% reflection on each endface is 0.36 dB loss
/4
0.2°
Relative position:
Axial separation
Preparation of end face:
Surface roughness
Angle
Extrinsic

## Slide 5: Process challenges: Insertion loss
Relative position:
Lateral off-set
Axial tilt
Extrinsic

## Slide 6: Process challenges: Insertion loss
Differences in:
Core diameter
Numerical
aperture
Refractive
index profile


Intrinsic

## Slide 7: Connection technologies: Non-detachable
Operational principle
  The cleaned and cleaved fiber are brought together as closely as possible in a splicing device (if possible without horizontal or vertical displacement). Subsequently, the splice area is protected with a so-called splice protection and then deposited.
Direction

## Slide 8: Connection technologies: Quasi-detachable
  Operational principle
    Two precisely cleaved pieces of fiber are butt-joint
    To improve the performance there is a so-called index matching gel between the two fiber
Fiber
Index matching gel
Fiber
Cap
Jacket
Fiber Size Designation Circles
(1/4 circle for 250µm coating, full circle for 900µm coated fiber
End Plug
Fiber Entry Port

## Slide 9: Connection technologies: Detachable
Operating principle
  Connector/adapter/connector principle
There are various types of end face polishes, differing in performance (RL, IL). They are:
    Flat
    Physical contact (PC)
    Angled Physical Contact (APC)
    Lens

## Slide 10: The perfect connection: first a high precise ferrules
The ferrule takes up the fiber and guides it concentric into the sleeve
The ferrule material must be corrosion less and rub off stable
Standard ferrule diameter is 2.5mm (SC, E2000, FC, ST) or 1.25mm (LC, MU)
In the ferrule centre is a hole with a diameter of approx. 126µm (the actual size is a secret of the assembly quality)
126µm

## Slide 11: Fiber Optic connectors: the quality choice the ferrule
The first element of quality:
material
resistance, deformation
dimensions
short/long tip and guiding effects
finishing profile
no contact, PC/ APC
alignment
material, dimension, no alignment

## Slide 12: Contact area morphology: Flat polish no butting
Non - butting ferrules
No physical contact
4% reflection on each endface results in 0.36 dB of loss
Transmission specifications
Insertion loss
Return loss
< 1.0 dB
~ 15 dB

## Slide 13: Contact area morphology: Physical Contact (PC) butting
Butting ferrules
Spherical physical contact
Transmission specifications
Insertion loss
Return loss
< 0.5 dB
> 20 dB
Radius 10 - 25 mm

## Slide 14: Contact area morphology : Angled Physical Contact polish
Butting ferrules
Angled spherical physical contact
Radius 5 - 12 mm
Angle 8 - 12°
Transmission specifications
Insertion loss
Return loss
< 0.3 dB
> 60 dB

## Slide 15: The perfect connection: ferrule – sleeve – ferrule coupling
Ferrule – sleeve – ferrule principal with physical contact of the convex polished end faces.
Keying system on the connector body prevent relative rotation of the end face
Adapter & sleeve

## Slide 16: Connection technologies: ferrule – sleeve – ferrule coupling
The 2 connectors are plugged into 1 adapter
Structure principle (of 2.5 mm ferrule)
Alignment technologies
resilient sleeve
Ferrule
Ferrule
Sleeve
Tolerance fields
Ferrule 2.4985 - 2.4995 mm
Sleeve gauge retention force 2.9 - 5.9 N
Materials
Ferrule ceramic (Zirconia)
Sleeve ceramic (Zirconia)  SM
PhBr  MM
Fiber
Sleeve
Fiber

## Slide 17: Quality of joining process: connector type
Choice driven by:
  application MM or SM
  active component
  standard requirements
  environment
Connection technique driven by:
  availability of skill and tools
  cost
  business reasons

## Slide 18: Connectors with a 2.5mm ferrule
FC connector
Threading mounting system. Keyed body for repeatability and intermateability. Primarily used with Singlemode fibers
SC connector
Snap-in locking mechanism for positive latching keyed body for repeatability and intermateability. Used for both - Singlemode and Multimode applications
ST connector
One-piece bayonet mounting system – easy to assemble. Mainly used with Multimode fibers

## Slide 19: Connectors with a 2.5mm ferrule
LSH connector
Also known as E-2000TM. Features a latched snap-in locking mechanism. Keyed body for repeatability. Exchangeable lever for either colour and/or mechanical coding. Integrated and self closing dust cap to protect ferrule endface.

## Slide 20: Duplex versions (2.5mm ferrule connectors)
LSHRJ
SFF - Small Form Factor connector. LSH simplex features fully integrated (except mechanical coding system). Ideal for high-density applications.
SCRJ
SFF - Small Form Factor connector. Smallest SC Duplex available. Snap-in locking mechanism and keyed body. Primarily used with Multimode fibers. Ideal for high-density data transmission applications.
SC Duplex
Snap-in locking mechanism for positive latching keyed body for repeatability and intermateability. Used for both - Singlemode and Multimode applications

## Slide 21: Connectors with a 1.25mm ferrule
LC connector
MU connector
Latched push-pull locking mechanism. Half the size of standard connectors. For private (primarily Multimode) and public (Singlemode) networks
For multiple optical connectors and self-retentive mechanism used in backplane applications. For high-speed data communications, voice networks and DWDM applications.

## Slide 22: Connectors with a 1.25mm ferrule
LX.5 connector
F-3000TM connector

## Slide 23: Connectors without “standard” ferrules
MTRJ connector
MTP connector
Flat rectangular “ferrule” for up to 12 fibers per connector. MTRJ is primarily used with Multimode fibers but Singlemode is seen also. MTP is a MPO compatible connector used very often in combination with ribbon fibers respectively where high packing density is required.
Notes: Optical values to reach are limited.

## Slide 24: Old connectors used for LAN applications
FDDI connectors
  FDDI/ST adapters
  FDDI/FDDI adapters
ESCON connectors (IBM applications)
  ESCON/ST adapters
  ESCON/ESCON adapters
FC/PC connectors
  FC/FC adapters
  FC/ST adapters
SMA connectors
  SM/SMA adapters

## Slide 25: Thank you
http://www.porta-optica.org
Piotr Turowicz
Poznan Supercomputing and Networking Center
piotrek@man.poznan.pl
Training Session

## Slide 26: References
Reichle & De-Massari