## Slide 1
LIGHT EMISSION / DETECTION
Lasers and LED Passive Elements
Piotr Turowicz
Poznan Supercomputing and Networking Center
piotrek@man.poznan.pl
Training Session
9-10 October 2006
.
http://www.porta-optica.org

## Slide 2: LIGHT EMISSION / DETECTION
Transmission
channel
Tx
E
O
Rx
O
E
Receiver
Converter
Transmitter
Converter
The principle of an optical communication system

## Slide 3: Wavelength range of optical transmission
Wavelength [nm]
Frequency [Hz]
2x1014
3x1014
5x1014
1x1015
Infrared
range
Visible
range
Ultraviolet
range
Fiber optic transmission range
Glass Plastic
850 -1630 nm 520-850 nm
1800 1600 1400 1200 1000 800 600 400 200

## Slide 4: From electricity to light
Conversion from electricity to light is achieved by a electronic :
  LED (light emitting diode)
  VCSEL (Vertical Cavity Surface Emitting Laser)
  LASERS FP (Fabry - Perot)
That:
  changes modulated electrical signal in light modulated signal
  inject light into fiber media

## Slide 5: Light emitters characteristics
Main characteristics for transmission purposes:
  1 Central wavelength
    (850/1300/1550)
  2 Spectrum width (at ½ power)
  3 Power
  4 Modulation frequency
(consequence of slope)
1
Wavelength nm
Power dB
3
2
Power/2
4

## Slide 6: Spectrum of a LASER or LED source
+5 to -10dBm
LASER
1-5nm
λ
LED
Density
-15 to -25 dBm
60-100nm
λ
Different frequency = different wavelength = different colors

## Slide 7: Power
Is the level of light intensity available for transmission
Average power is the mean value of the power during modulation
Power available for transmission is also function of:
  Fiber core size
  Numerical aperture
Light entrance cone
N.A.
(Numerical Aperture)

## Slide 8: Modulated frequency
Is the rate at which transmission changes intensity (logical 0 to 1)
  Rate is function of time
  Time is function of slope
  Slope is characteristic of emitter (technology)
    LED functions at lower frequency (longer time)
    LASERS at higher (shorter time)
    TIME influences modal bandwidth

## Slide 9: Emitters comparison
Type | Cost | Wavelength (nm) | Spectral width (nm) | Modulated frequency | Power (dBm) | Usage
LED | $ | 850-900 1250-1350 | 30-60 < 150 | < 200 MHz | - 10 to -30 | F.O. systems
Short Wavelength Lasers | $$ | 780 | 4 | ≥ 1GHz | +1 to -5 | CD Fiber Ch.
VCSEL | $$ | 850 1300 | 1 to 6 | ≈ 5GHz | +1 to -3 | F.O. Giga speed
Lasers | $$$ | 1300 1550 | 1 to 6 | ≥ 5GHz | +1 to -3 | F.O. SM

## Slide 10: Emitter characteristics transmission related effects
LED
VCSEL
LASER
Over Filled Launch (OFL)
Restricted Mode Launch (RMF)
Restricted Mode Launch (RMF)
Emitters inject light into fiber under different conditions (emitter physical characteristic).
  Modes travel consequently Power is distributed consequently

## Slide 11: Emitters consideration
Splice
Multimode Fiber
MM
SM
Active
component
Rec
TX
Rec
TX
Cabling
Generally, emitters can be optimized for fiber they have to illuminate
  for example to reduce effects of DMD - “Differential Mode Delay” .
1000Base-LX is used on MM as well as SM
  VCSEL cannot be optimized.
DMD optimization is achieved by Conditioned Patch Cords

## Slide 12: The principle of an optical communication system
Transmission
channel
Tx
E
O
Rx
O
E
Receiver
Converter
Transmitter
Converter

## Slide 13: From light to electricity
Conversion from light to electricity is achieved by photodetector/receiver that:
  is triggered by modulated light
  transforms modulated light into modulated electrical signal
Transmission characteristics are:
  Sensitivity
  Dynamic range
  BER

## Slide 14: Receiver characteristic
Sensitivity
  is the minimum power that is detected by the receiver with BER level
BER
  is the max allowed error counted in bit in error/bit transmitted
    BER is function of sensitivity among others characteristics
Dynamic range
  Is the maximum average power received to maintain BER
    Too much power causes distortion and saturation
    Too less power causes no bit received
      Both causes BER in excess of specified limit
      Dynamic range is expressed as difference between min. and max.

## Slide 15: Spectral sensitivity of detectors
Material used in electronic manufacturing determine the sensitivity
Technology and temperature regulate response in amplitude and time (slope)

## Slide 16: Bandwidth limitations dependent on electronics
Switching time (or rise time, or slope) is affecting the width of the signal
Width of signal is determining the spreading of the signal
Signal spreading is the cause of bandwidth limitations
Bandwidth limitation in a fiber channel is therefore function of:
    fiber bandwidth (known factor)
    contribution of electronic (active components dependent)
    Length of the channel (known or to be calculated)
Complex equation
Standard

## Slide 17: Passive FO elements
http://www.porta-optica.org

## Slide 18: Passive elements
Passive elements in Optical Network:
  Optical fiber
  Spliter/combiner
  MUX/DMUX
  Add MUX
  Fiber Bragg grating based devices
  Circulator
  Isolator
  Lens
  Attenuator

## Slide 19: REQUIRED OPTICAL CHARACTERISTICS
In general, multiplexer/demultiplexers for DWDM are
required to have the following optical characteristics:
• Small center wavelength offset from grid wavelength
  The permissible center wavelength offset depends on the transmission spectrum of the MUX and the transmission bit rate of the system, but is normally not more than 0.05 nm.
• Low insertion loss
  As in the case of other FO transmission devices,insertion loss should ideally be as low as possible
• Low channel crosstalk
  Channel crosstalk in terms of a specific MUX channel n is expressed as the difference between the insertion loss at the grid wavelength n of channel n and the insertion loss at the grid wavelength of the respective channel. Channel crosstalk should be as low as possible (-25 dB or better)

## Slide 20
splitter
combiner
1
2
3
4
coupler
star coupler
λ1+λ2
λ 2
λ 1
wavelenght multiplekser
λ1+λ2
λ 1
λ 2
wavelenght demultiplekser

## Slide 21
lustro
półprzepuszczalne
F1
F2
F3
1
2
3
4
Fibers optic
mixer-rod
mixer-rod
mirror

## Slide 23
Polishing coupler
Melting and stretching coupler
Coupler based on planar lightwave circuit (PLC) technology
Stage of coupler manufacturing

## Slide 24
MUX / DMUX
Fiber IN
Fiber OUT
Lens
Diffraction
gratting

## Slide 25
Wavelenght filters
1
2
1, 2
lens GRIN
Filter
b)
filter
1, 2
2
1
Fiber IN
GRIN lens

## Slide 26: MUX
Optical waveguide circuit structure of AWG

## Slide 27: Lens GRIN
Microptic elements:
GRIN Lens - GRadient INdex Lens
SELFOC - self focusing
NA2
NA1
Fiber
Source
Dimensions:
Lenght: 3–30 mm
Diameter: 1-2 mm

## Slide 28: Isolator
Magnetooptic material
H - magnetic field strength
paramagnetic
lens
mirror
lens
Optical prism
Optical prism
magnet
light beam

## Slide 29: Attenuators

## Slide 30
Fiber Bragg dispersion compensator
Principle

## Slide 31: References
Reichle & De-Massari