## Slide 1
Optical Budget
http://www.porta-optica.org
Piotr Turowicz
Poznan Supercomputing and Networking Center
piotrek@man.poznan.pl
9-10 October 2006

## Slide 2: Introduction
When planning a new network or expanding an existing
one with WDM equipment, one of the first things to consider is
the distance between the equipment nodes.
Distance is related to fiber-optic parameters like:
      dispersion
      attenuation.
Precise attenuation calculations should take place at the planning stage.
The actual fiber optic cable attenuation should be measured
or calculated based on the cable vendor specifications and
the network segments distances.

## Slide 3: Technical design elements: Terminology
Decibels (dB) – used for power gain or loss
Decibels-milliwatt (dBm) – used for output power and receive sensitivity
Attenuation – loss of power in dB/km
Chromatic dispersion – spreading of the light pulse in ps/nm*km
Bit Error Rate (BER) – typical acceptable rate is 10-12
Optical Signal to Noise Ratio (OSNR) – ratio of optical signal power to noise power for the receiver
ITU Grid Wavelength – standard for the lasers in DWDM systems

## Slide 4: Technical design elements: Decibel scale
The decibel (db) represents the logarithmic relation
of two power levels P1 and P2 usually measured in watts.
dB=10log(P1/P2)
Decibels also can measure power relative to certain levels.
For example, when P2=0.001 Watt,
the value units will be called “dBm”,
which means power related to 1 milliwatt.
dBm=10log(P1/1mW)

## Slide 5
Technical Design Elements: Optical Budget
Optical budget = Output power – Input sensitivity
Optical budget is affected by:
  Fiber attenuation
  Splices
  Patch panels / connectors
  Optical components (filters, amplifiers, etc.)
  Bends in the fiber
  Contamination (dirt, oil, etc.)

## Slide 6
Technical Design Elements: Power Penalties
Penalty Ranking:
Fiber loss (attenuation)
Splices
Connectors
Dispersion Penalties
Fiber Nonlinearities Penalties
Component / Fiber Aging Penalties
Transforms the signal
from this to this
High to Low

## Slide 7
Technical Design Elements: Penalties
Attenuation: pulse amplitude reduction limits “how far”
Chromatic Dispersion: spreading of the pulse from different colored light traveling at different speeds within the fiber
Polarization Mode Dispersion: spreading of the light pulse from fast and slow axes having different group velocities

## Slide 8: Fiber attenuation measurements
Fiber optic cables perform differently at various wavelengths,
so it’s cardinal to set the power meter at the correct wavelength
as well as to match it with the light source.
For example, WDM technology uses the 1550 nm region,
so it’s more practical to test the cable with the same wavelength
of 1550 nm, if we plan to use it for WDM transmission

## Slide 9: Fiber attenuation measurements
The first step is measuring the launched power from the transmitting device. Using “launch patch” instead of a direct connection to the transmitter eliminates the influence of the transmitter - cable connection attenuation.

## Slide 10: Fiber attenuation measurements
The cable under test will connect between the “launch patch” and the “receive patch”, in order to eliminate any non-cable related attenuations.

## Slide 11: Fiber attenuation measurements
Cable attenuation = (-3dbm) - (-10dbm) = 7db

## Slide 12: Optical network attenuation
Without amplification, the maximum allowable loss in an all-optical network is given by the difference between the launch power and the receiver sensitivity.
Allowable loss (dB) = Tx_power – Rx_sensitivity
Of course, this value is true only if we connect transponders directly to the transmission fiber.

## Slide 13: Optical network attenuation
It is very useful to be able to specify in dB an absolute power wi watts or in mW
To do this the power P2 in the dB formula is fixed at some agreed reference value, so the dB value always relates to this reference power level.
Allows for easy calculation of power at any point in a system
Where the reference power is 1mW the power in an optical signal with a power level P is given in dB as:
Power [dB] = 10 Log [P/1nW]

## Slide 14: dBm calculation (Transitter)
A transmitter laser has a measure output power of 2.3mW. What is the laser diode output power expressed in dBm?
Transmitter laser
2.3mW
Power [dB] = 10 Log (Power /1 mW)
Power [dB] = 10 Log (2.3mW /1 mW)
Power [dB] = 10 Log (2.3) = +3.61dBm

## Slide 15: dBm calculation (Transitter)
dB and dBm can be combined in the same calculation
As shown a fiber span (inc. splices etc.) has a total attenuation of 13 dB
If the trasmitter output power is +2 dBm what is the reciver input power in dBm?
Transmitter
Fiber span: att 13dB
Reciver
+2 dBm
? dBm
Reciver input [dB] = Transmitter output power – Total fiber span att.
Reciver input [dB] = +2 dBm – 13 dB
Reciver input [dB] = -11 dBm

## Slide 16: Point-to-Point link attenuation calculation
Components
Fiber SM 9/125 14 km at 0.25dB 3.5
Connector 3 pcs. at 0.5dB 1.5
Splice 6 pcs. at 0.1dB (0.15dB) 0.6___
Total attenuation 5.6 dB
Connection
Splice
Connection
Connection
4 km
2 km
3 km
TX
RX
5 km

## Slide 17: Point-to-Point link attenuation calculation
The table contains some typical numbers, which can be used to approximate optical link budget calculations. If at all possible, real numbers from the network in question should be used.
Standard for connector loss | 0.5 dB
Typical cable attenuation at 1310nm | 0.4 dB
Typical cable attenuation at 1550nm | 0.25 dB
Typical splice attenuation | 0.1 dB
Typical distance between splices | 6 km
Typical safety margin | 3 dB
*) CD penalty | 1 dB

## Slide 18: Optical Budget Calculator
Minimum Transmit Power _________
    Minimum Receive Sensitivity _________
    Available Power = _________
    _________ Km of cable X _________ dB/km = _________
    _________ Connectors X _________ dB/Con. = _________
    _________ Splices X _________ dB/splice = _________
    Link Margin = _________
    _________ Repair Splices X _________ dB/Splice = _________
    Safety Margin _________
    Excess Power _________

## Slide 19: Optical Budget Calculator

## Slide 20: References
Reichle & De-Massari
http://www.porta-optica.org